## Slide 1: Introduction to 3D Printing
Bainbridge Artisan Resource Network
Electronic & Technical Arts Studio

## Slide 2: Objectives
Learn what 3D printing is and how it works
During class …
  Acquire a 3D model to print
  Prepare the model to be printed
  Print it
After class …
  Be able to become certified to use BARN’s 3D printing facilities on your own
  Learn more advance techniques either through additional BARN classes or through self-guided learning (YouTube, et al.)

## Slide 3: Agenda
3D Printing … what it is and what it is not
Workflow ... from model to finished print
  Preparing the model to be printed
  Loading the file, setting-up the printer, starting the print
  The finished results
Additional Topics
  Finding and downloading a model
  Creating a model from scratch (superficially covered)

## Slide 4: What is 3D Printing?
An Additive Manufacturing process
  Material is added in layers
  Wide variety of materials: plastics, metals, glass, ceramic, food, …
  Printed through a variety of processes: heat, lasers, ultraviolet, …
  At the bleeding edge: printed organs, exotic food presentation, prosthetics … limited only by imagination.
At BARN, 3D printing is …
  Melted plastics extruded through a heated nozzle (much like a glue gun)
Misconceptions and cautions
  You can’t print everything
  It may take some tweaking of printer settings
  Size is limited
  Prints can take a long time

## Slide 5: 3D Printer Workflow at BARN
3D Design App
Internet Sources
Ultimaker 2+
Cura
Slice
Download
Your Computer
SD Card
.stl
model
. gcode sliced model
Design

## Slide 6: Prepare 3D Model for Printing
.stl
model
. gcode
sliced model
3D Design App
Internet Sources
Ultimaker 2+
Cura
Slice
Download
Your Computer
SD Card
Design
Prepare 3D model

## Slide 7: The model file
Computer generated file
  .stl file type (stereolithography)
  Almost universally used at BARN and elsewhere
Defines the surface geometry
  Surface is defined by linked triangles
  Following is an .stl example of a sphere in different resolutions

## Slide 8: The Sliced Model
Computer generated file
  .gcode file type
  File format support a layer-by-layer manfacturing process
    Originally for subtractive manufacturing (e.g., CNC Routing/Machining)
    gcode for 3D printing is a derivative of the original gcode
Defines how the printer should behave
  Horizontally slices the model into layers
  For each layer, it defines print-head movement and actions

## Slide 9: Slicing The Model
A software program to converts the 3D model (.stl) into a printable model (.gcode)
It specifies things like layer height, speeds, infill density
There are lots of different slicer programs.
  Cura, Slic3r, MatterControl, KISSicer
At BARN with the Ultimaker2+, we use Cura
.stl model defines the surface geometry
Cura creates a layer-by -layer definition
.gcode controls each level of the printing process

## Slide 10: Slicing The Model
Cura needs to know about …
  Printer and the nozzle being used
  Material being used
We will focus on basic settings
  Nozzle size (0.4 mm) > preset and OK
  Material (typically SLA) > you set
  Profile (predefined settings) > you set
    High Quality +++ quality print time: 3x Fast setting
    Normal Quality ++ quality print time: 2x Fast setting
    Fast Print + quality print time: fastest
These settings work for the majority prints

## Slide 11: Using Cura
File Name
Size
Print Time

## Slide 12: Using Cura
Model maximums
  Maximum size is 223 x 223 x 205 mm (8.8 x 8.8 x 8.1 inches)
  BUT the time to print this would be measured in days
Additional resources
  Cura manual:
  Learning Cura

## Slide 13: Printing the Model
.stl
model
. gcode
sliced model
3D Design App
Internet Sources
Ultimaker 2+
Cura
Slice
Download
Your Computer
SD Card
Design
Print the model

## Slide 14: Material Used
Material is referred to as Filament
Wide range of material types to choose from
Three typical diameters
  1.75 mm, 2.85 mm, 3.0 mm
Material type, diameter and other recommended printer settings are written on each spool
Note: The filament available for 3D printing at BARN has been provided by individual members of ETA. Unless a spool is otherwise marked, it is available to be used by a BARN member. If you plan to become active in 3D printing, please consider contributing a spool to the studio cache. You could replace a spool that is running low or add a new/novel color or material.

## Slide 15: Material Used
PLA (polylactic acid) | The most widely used; recommended for beginners. Prints fast, is safe, can be used for a broad range of models and applications. (Most commonly used at BARN).
Nylon (polyamide) | Widely used by manufacturers for strong end-use parts and functional prototypes requiring durability and abrasion resistance.
ABS (acrylonitrile butadiene styrene) | Frequently used. Good mechanical properties; can be used for a wide range of applications. *Requires ventilation during printing.
CPE (co-polyester) | Chemical resistant, relatively tough material widely used for functional prototyping and modeling.
PVA (polyvinyl alcohol) | Used to create water soluble support structures to achieve complex geometries.
PC (polycarbonate) | Very strong and tough material used for various engineering applications.
TPU (thermoplastic polyurethane) | Semi-flexible; used in a wide variety of engineering projects where easier and faster printing is more important than aesthetic qualities.
More details at all3dp.com: 3D Printer Filament Guide & Comparison

## Slide 16: Setup Printer
Load SD Card
  tbd
Load Material
  tbd

## Slide 17: Setup Printer (continued)
Select and print model
  tbd

## Slide 18: The Finished Print
Tbd – discuss print fails (not in depth)

## Slide 19: Find Existing 3D Models
.stl
model
. gcode
sliced model
3D Design App
Internet Sources
Ultimaker 2+
Cura
Slice
Download
Your Computer
SD Card
Design
Find 3D models

## Slide 20: Existing 3D Sources
What to look for
  Something useful
    Household items
    Tech items
    Tools and gadgets
    Storage and organization
Top sites
  thingiverse.com
  instructables.com
  youmagine.com
  yeggi.com
  Google says … “top sites for 3d models”
  Something for kids
    Pokemon figures
    Custom Lego blocks
    Other toys
    Educational items

## Slide 21: Design a 3D Model
.stl
model
. gcode
sliced model
3D Design App
Internet Sources
Ultimaker 2+
Cura
Slice
Download
Your Computer
SD Card
Design
Design a model

## Slide 22: 3D Design Apps
  3D modelling software can range from fairly easy to quite difficult to learn
  Thingiverse post … “Which 3D software for 3D printing?” (Note: source for above chart)
  Google says … “best 3d modeling software for 3d printing”
App | Level | Use | Comments
TinkerCAD | Beginner, Intermediate | Precise shapes | Starting point for beginners, yet provides good capabilities
Fusion 360 | Intermediate, Advanced | Precise shapes | Fairly long learning curve, but many adherents
OpenScad | Intermediate | Precise shapes | 3D design through programming/scripting
DesignSpark Mechanical | Intermediate | Precise shapes | Choice of Thingiverse poster
Blender | Advanced | Organic designs | Most comprehensive with longest learning curve

## Slide 23: Next Steps
tbd – list of upcoming ETA classes for BARN

## Slide 24: Terminology
Low-Poly
  Models created with low polygon counts for artistic effect or speed of rendering
Photogrammetry
  A fully textured 3D model created from a series of photographs of a real object
Rigged Model
  The process of making an object ready for animation where there is an internal structure coordinated with the mesh surface that can mimic natural movements
Voronoai Model
  A model in which only the interconnecting edges of the surface mesh are printed
Note: Derived from more extensive glossary at http://www.brianschrank.com/2730/maya/3dglossary.pdf and elsewhere.